## Slide 1
OpenHW CVA5 RISC-V Soft Processor
RTL/SW → Running Simulation → Hello World on FPGA
Amirali Ebrahimi github.com/AmirAliEbrahimi/cva5
Notes: Hi everyone, quick 5 minute status on the CVA5 work, then two short demos: one in simulation and one live on the FPGA board.

## Slide 2
About me
Amirali Ebrahimi
Digital Design Engineer
github.com/AmirAliEbrahimi
FPGA / ASIC RTL, front-end design
Almost 5 years of design and verification
Embedded systems
From Machine Code to End-user Application
FPGA & soft IP MCUs on the side
x86, SPARC, RISC-V, and more
Notes: Quick intro. I do FPGA and ASIC RTL, front end design, almost 5 years. My background covers embedded systems, and on the side I play with FPGAs and soft IP MCUs.

## Slide 3
The goal: CVA5 anyone can pick up in a weekend
An onboarding path to RISC-V with no FPGA background assumed
Self contained
A clean clone runs in simulation with two make commands. No Taiga project or any external build framework needed.
Modular blocks
The project is split into small blocks that work as tutorials: spec, then code, then simulation/implementation
End goal
Anyone can implement a new feature on the CVA5 and see it run in simulation and on hardware.
Taiga project: Top-level system wrapper and the full build environment (toolchain, test suites, setup scripts) for the CVA5 Processor https://gitlab.com/sfu-rcl/taiga-project
Notes: The framing here is a slow burn: paced so anyone can catch up in a weekend. The flow is self contained, so you do not need the Taiga project environment anymore. The simulation gets split into blocks that work as tutorials, and the end goal is that someone with no FPGA background can add a feature to CVA5 themselves.

## Slide 4
The plan
Where we are and where this goes
Q3 2026
Q4 2026
Q1 2027
Q2 2027
this update
Ramp up on CVA5
Verilator simulation
Compiler to memory image flow
CVA5 running on FPGA
Onboarding
Develop the onboarding and ramp up process for new adopters of CVA5.
The goal is to add a new feature to CVA5, for example TinyAI.
Also CVA5 software on QEMU or Renode.
Conference
Prepare a paper, poster, presentation and demo for a conference
TBD
Initial SW stack
Register map, bare metal boot code and APIs (SDK).
Instructions for developing a board support package (BSP) for CVA5 on different FPGA evaluation boards.
Notes: Here is the plan. We are in Q3: ramp up on CVA5 far enough to demo at the RVO user group meeting. That is the Verilator simulation, the compiler to memory image flow, and CVA5 running on FPGA. The next two slides are exactly those demos. Q4 is the onboarding and ramp up process for new adopters, and the goal there is that someone can add a new feature to CVA5, TinyAI being the example we have in mind. Q1 is a conference paper, poster and demo, and the venue is still to be decided. Q2 is the initial software stack, and that is also where QEMU or Renode support lands. We do not have that yet.

## Slide 5
Demo 1 — Simulation: compiler → hardware
Verilator model · waveform and UART console output
What you'll see
make sim && make run
A tiny C program prints Hello World. In the waveform we follow each character from the store instruction to the UART register and out on the TX line.
The work a compiler does, all the way down to hardware.
Every stage is a file you can open
main.c, crt0.S C source and startup code
main.elf gcc output, then objdump gives the asm listing
program.hex, mem.mif objcopy to raw binary, then the memory init file
$ cd examples/sw
$ make sim # build Verilator model
$ make run # compile C, run on sim
cva5-sim <log> <sig> <program> <trace>
Hello World!
Hello World!
Hello World!
sim done: addi x0,x0,10 retired
$ gtkwave trace.fst # live waveform →
Notes: Demo 1, in simulation. Two make commands from a clean clone. First I'll walk the build one stage at a time, because every stage is a file you can open: main.c and crt0.S go in, gcc links them into main.elf, objdump turns that into an assembly listing so you can read the actual instructions, and objcopy strips it down to the raw binary that becomes program.hex for the simulator and mem.mif for the FPGA block RAM. Same file, two destinations. Then the console output, Hello World over the simulated UART. Then the wavefile: the register write to the UART address, the bus transaction, the TX line toggling. That is the whole point, watching the work a compiler does all the way down to hardware. [SWITCH TO DEMO 1: build stages, waveform and sim output]

## Slide 6
Demo 2 — FPGA: same program, real silicon
PYNQ-Z2 (Zynq-7020) · Vivado 2025.1 · live UART output
What you'll see
clk_wiz
125→100 MHz
reset
SW0 switch
CVA5
RV32IM + BRAM
AXI UART
Lite
9600 8N1
Same binary, both worlds. program.hex for simulation and mem.mif for the FPGA block RAM share one format. make mif rebuilds the FPGA image straight from main.c.
PuTTY — COM4 @ 9600 8N1
Hello World!
Hello World!
Hello World!
Hello World!
one line per second,
usleep() timed to the
100 MHz core clock
SW0 ↓ reset · ↑ run
Notes: Demo 2, on hardware. The same program running on the PYNQ-Z2. Two Tcl scripts build the whole SoC: clock wizard, reset from slide switch SW0, CVA5 with the program in block RAM, and an AXI UART Lite. The board's USB UART is wired to the PS, so the PL UART is jumpered from PMOD JA to J13 with two wires, and the same micro USB cable then programs the board and carries the console. I'll flip SW0 and show live Hello World in the terminal. [SWITCH TO DEMO 2: Vivado project and live UART] To close: that is the Q3 milestone from the plan slide. Next up is the onboarding process, and the fork link is in the deck. Questions welcome. Thanks!